## Slide 1
CROWDSHIELD: EDGE-AI DENSE CROWD SENTINEL & AUTONOMOUS EGRESS ROUTING
Dual-Radio Hardware Mesh Spine for Mass Pilgrimages & Extreme Gathering Safety
Raghunandhan P. [Reg: 21BCEXXXX] | Student 2 | Student 3
Project Mentor: Prof. X. Xxxxxxxxxxxx | School of Computer Science and Engineering (SCOPE)
SDGs Addressed:
SDG 3: Good Health & Safety
SDG 9: Resilient Infrastructure
SDG 11: Sustainable Cities
Motivation / Introduction
Problem Statement
At massive indoor gatherings like the Maha Kumbh Mela, Puri Rath Yatra, or temple festivals, crowd density regularly exceeds 5 to 8+ persons per square meter (p/m²). At this extreme scale, two catastrophic failure modes occur simultaneously.
▪ Bounding-Box Vision Breakdown: Standard object detection (regular YOLO) fails completely because individual human bodies occlude into an unbroken ocean of millions of overlapping heads.
▪ Cellular Blackout: When 50+ lakh devotees congregate, mobile towers and internet backhauls fail, rendering all cloud-dependent computer vision APIs unreachable.
CrowdShield addresses this life-critical gap through a 100% offline edge-computing command spine that couples density-map regression vision with a localized dual-radio mesh that functions autonomously without Internet connectivity.
Scope of the Project
Objectives
▪ Adaptive 4-Tier Vision Orchestrator: Dynamically switches inference between YOLOv8 (sparse flow), P2PNet (head-dot click analysis), CSRNet (dilated density regression >5 p/m²), and DM-Count (haze/dust scenes).
▪ Dynamic Topological Egress Optimization: Integrates a hazard-aware network GIS graph that automatically severs blocked corridors (like a stampede) and computes the safest path using Dijkstra's algorithm.
▪ Zero-Cloud Hardware Spine: Deploys field nodes powered by ESP32 microcontrollers, 1602 LCDs, DFPlayer Mini voice annunciators, and 433 MHz LoRa / 2.4 GHz ESP-NOW dual radios.
Key Achievement: 100% Offline Real-Time Execution at 18–28 FPS with sub-second localized hardware actuation latency across field nodes.
Mathematical Modeling
Homography & Graphs
A. 4-Point Planar Perspective Homography Matrix: converts pixel coordinates (u, v) to real-world ground meters (xₘ, yₘ) via a 3×3 homography H.
B. Continuous Density Surface Integration: continuous head regression over GIS polygon zone Z:
C. Hazard-Penalized Dynamic Routing Cost:
Conclusion / Summary
Summary
CrowdShield establishes that ultra-dense crowd safety does not require cloud connectivity or expensive optical infrastructure. By integrating dilated convolutional density maps with an autonomous dual-radio wireless mesh, the system provides sub-second localized audible guidance, isolating stamped or burned zones in real time.
References (APA Format)
Li, Y., Zhang, X., & Chen, D. (2018). CSRNet: Dilated convolutional neural networks for understanding the highly congested scenes. CVPR, 1091–1100.
Song, Q., et al. (2021). Rethinking counting and localization in crowds: A purely point-based framework. ICCV, 3365–3374.
Wang, B., Liu, H., et al. (2020). Distribution matching for crowd counting. NeurIPS, 33.
Methodology
End-to-End Pipeline
The architecture decouples heavy neural computation from field radio downlinks via an asynchronous FastAPI engine and distributed hardware gateways.
Fig. 1. End-to-end CrowdShield pipeline from ingest to hardware actuation.
Architectural Subsystems:
a) CSRNet Dilated Convolutions: Uses a VGG-16 backbone with 4 dilated convolution layers (dilation rate r = 2) to expand the receptive field without downsampling, maintaining pixel-accurate density estimation during severe body occlusion.
b) P2PNet Direct Head Localization: Predicts exact 2D point coordinates on human head crowns with cross-entropy and Hungarian matching, feeding precise spatial coordinates to the venue homography.
c) Hardware Fault Tolerance: The gateway auto-connects over USB Serial (115200 baud). Zonal nodes incorporate anti-brownout bulk capacitors (1000 µF), a non-blocking FreeRTOS yield() watchdog reset, and 2.5 s playback debounce filters.
Results
Model Benchmarks
Architecture Tier | Density Threshold | FPS | MAE | Accuracy
YOLOv8 Head Tracking | < 2.5 p/m² | 28.4 | 3.4 | 94.6%
P2PNet Point Locator | 2.5 – < 5.0 p/m² | 16.1 | 4.8 | 91.0%
CSRNet Density Map | > 5.0 p/m² (Crush) | 19.0 | 3.1 | 96.2%
DM-Count (Haze/Dust) | Perspective Choke | 11.2 | 3.5 | 92.4%
Table 1. Performance metrics of vision models across distinct crowd densities.
Fig. 2. Accuracy vs crowd density.
Fig. 3. Evacuation clearance curves.
Network Layer | Latency | Packet Delivery | Cloud Dependency
2.4 GHz ESP-NOW Mesh | 4.2 ms | 99.4% | 0% (100% Offline)
433 MHz LoRa SX1278 | 120 ms | 98.8% | 0% (100% Offline)
Cellular 4G/5G (Jammed) | 1,840 ms | 24.1% (Blackout) | 100% (High Risk)
Table 2. Dual-radio transmission metrics vs cellular baseline.
Contact: raghunandhan.p2020@vitstudent.ac.in | Mentor: faculty_guide@vit.ac.in | Venue: SCOPE / SENSE Capstone Project Expo, VIT Vellore